## Slide 1: Today’s Contents
Sharpening spatial filtering
  1st derivative filters
  2nd derivative filters
Derivatives of Image
Laplacian Filter
Laplacian Image Enhancement
Difference filters
Combining filtering techniques
Chapter 3 from R.C. Gonzalez and R.E. Woods, Digital Image Processing
(3rd Edition), Prentice Hall, 2008 [ Section 3.6, 3.7 ] https://www.quora.com/How-can-we-find-the-shortest-m-connected-path-if-
the-pixel-values-are-given-in-matrix-form http://www.cse.iitm.ac.in/~vplab/courses/CV_DIP/PDF/NEIGH_CONN.pdf

## Slide 2: Sharpening Spatial Filters
DIP, Spring 2012 GS & AS, Bahria University, Islambad
Previously we have looked at smoothing filters which remove
fine detail
Sharpening spatial filters seek to highlight fine detail
Remove blurring from images
Highlight edges
Sharpening filters are based on spatial differentiation

## Slide 3: Spatial Differentiation
DIP, Spring 2012 GS & AS, Bahria University, Islambad
Sharpening filters are based on first- and second-order derivatives of image.
The derivatives of a digital function are defined in terms of differences.
i.e. Sharpening filters are based on spatial differentiation

## Slide 4: Spatial Differentiation
DIP, Spring 2012 GS & AS, Bahria University, Islambad
Let’s consider a simple 1 dimensional example

## Slide 5: Spatial Differentiation
DIP, Spring 2012 GS & AS, Bahria University, Islambad
A B

## Slide 6: 1st Derivative
DIP, Spring 2012 GS & AS, Bahria University, Islambad
The 1st derivative of a function is given by:
Its just the difference between subsequent values and measures the rate of change of the function
x
f  f (x 1)  f (x)

## Slide 7: 1st Derivative
DIP, Spring 2012 GS & AS, Bahria University, Islambad
8
7
6
5
4
3
2
1
0
8
6
4
2
0
-2
-4
-6
-8
5 | 5 | 4 | 3 | 2 | 1 | 0 | 0 | 0 | 6 | 0 | 0 | 0 | 0 | 1 | 3 | 1 | 0 | 0 | 0 | 0 | 7 | 7 | 7 | 7
 | -1 | -1 | -1 | -1 | -1 | 0 | 0 | 6 | -6 | 0 | 0 | 0 | 1 | 2 | -2 | -1 | 0 | 0 | 0 | 7 | 0 | 0 | 0 | 

## Slide 8: 2nd Derivative
DIP, Spring 2012 GS & AS, Bahria University, Islambad
The 2nd derivative of a function is given by:
Simply takes into account the values both before and after the current value
f (x 1)  f (x 1)  2 f (x)
2 x
2 f 

## Slide 9: 2nd Derivative
DIP, Spring 2012 GS & AS, Bahria University, Islambad
8
7
6
5
4
3
2
1
0
5 | 5 | 4 | 3 | 2 | 1 | 0 | 0 | 0 | 6 | 0 | 0 | 0 | 0 | 1 | 3 | 1 | 0 | 0 | 0 | 0 | 7 | 7 | 7 | 7
10
5
0
-5
-10
-15
 | -1 | 0 | 0 | 0 | 0 | 1 | 0 | 6 | -12 | 6 | 0 | 0 | 1 | 1 | -4 | 1 | 1 | 0 | 0 | 7 | -7 | 0 | 0 | 

## Slide 10: 2nd Derivative for Image
DIP, Spring 2012 GS & AS, Bahria University, Islambad
Enhancement
The 2nd derivative is more useful for image enhancement
than the 1st derivative - Stronger response to fine detail
We will come back to the 1st order derivative later on
The first sharpening filter we will look at is the Laplacian

## Slide 11: Laplacian Filter
DIP, Spring 2012 GS & AS, Bahria University, Islambad
2 f 2 f f  2 x  2 y
2
2 x
2 f     
f (x 1, y) f (x 1, y) 2 f (x, y)
The Laplacian is defined as follows:
f (x, y 1)  f (x, y 1)  2 f (x, y)
2 y
2 f 

## Slide 12: Laplacian Filter
DIP, Spring 2012 GS & AS, Bahria University, Islambad
So, the Laplacian can be given as follows:
2 f  [ f (x 1, y)  f (x 1, y)
 f (x, y 1)  f (x, y 1)]
 4 f (x, y)
0 | 1 | 0
1 | -4 | 1
0 | 1 | 0
Can we implement it using a filter/ mask?

## Slide 13: Laplacian Filter
DIP, Spring 2012 GS & AS, Bahria University, Islambad

## Slide 14: Laplacian Filter
DIP, Spring 2012 GS & AS, Bahria University, Islambad
Applying the Laplacian to an image we get a new image that highlights edges and other discontinuities
Original Image
Laplacian Filtered Image
Laplacian Filtered Image
Scaled for Display

## Slide 15: Laplacian Image Enhancement
DIP, Spring 2012 GS & AS, Bahria University, Islambad
The result of a Laplacian filtering is not an
enhanced image
Laplacian Filtered Image
Scaled for Display
5
f (x, y) 2 f , w  0
5
f (x, y)  2 f , w  0
g(x, y) 
To generate the final enhanced image

## Slide 16: Laplacian Image Enhancement
DIP, Spring 2012 GS & AS, Bahria University, Islambad
In the final sharpened image edges and fine
detail are much more obvious
-
=
Original Image
Laplacian Filtered Image
Sharpened Image

## Slide 17: Laplacian Image Enhancement
DIP, Spring 2012 GS & AS, Bahria University, Islambad

## Slide 18: Simplified Image Enhancement
DIP, Spring 2012 GS & AS, Bahria University, Islambad
 The entire enhancement can be combined into a single filtering operation
g(x, y)  f (x, y)  2 f
 f (x, y) [ f (x 1, y)  f (x 1, y)
 f (x, y 1)  f (x, y 1)
 4 f (x, y)]

## Slide 19: Simplified Image Enhancement
DIP, Spring 2012 GS & AS, Bahria University, Islambad
 The entire enhancement can be combined into a single filtering operation
g(x, y)  f (x, y)  2 f
 5 f (x, y)  f (x 1, y)  f (x 1, y)
 f (x, y 1)  f (x, y 1)
0 | -1 | 0
-1 | 5 | -1
0 | -1 | 0
We can implement it using this filter.

## Slide 20: Simplified Image Enhancement
DIP, Spring 2012 GS & AS, Bahria University, Islambad
This gives us a new filter which does the whole job for us in one step
0 | -1 | 0
-1 | 5 | -1
0 | -1 | 0

## Slide 21: Variants On The Simple Laplacian
DIP, Spring 2012 GS & AS, Bahria University, Islambad
There are lots of slightly different versions of the Laplacian that can be used:
0 | 1 | 0
1 | -4 | 1
0 | 1 | 0
1 | 1 | 1
1 | -8 | 1
1 | 1 | 1
-1 | -1 | -1
-1 | 9 | -1
-1 | -1 | -1
Simple
Laplacian
Variant of
Laplacian

## Slide 22: Use of first derivatives for image enhancement: The Gradient
DIP, Spring 2012 GS & AS, Bahria University, Islambad
The gradient vector of a function f(x,y) is defined as
f 
 

y 
f 
G 
y 
f  Gx   x 

## Slide 23: Use of first derivatives for image enhancement: The Gradient
DIP, Spring 2012 GS & AS, Bahria University, Islambad
The magnitude of this vector is given by:
f  mag(f )
2
1
2 2
y
x
 G  G 
1
2  2
2
  

 

 y 
  f  
 x 
  f 
For practical reasons this can be simplified as:
f  Gx  Gy

## Slide 24: Use of first derivatives for image enhancement: The Gradient
25

## Slide 25: Gradient Operators
DIP, Spring 2012 GS & AS, Bahria University, Islambad
There is some debate as to how best to calculate these
gradients
Simplest Operator
8 5
6
5
f  (z8  z5 )  (z6  z5 )
x
y
f  (z  z ), f  (z  z )
y x
f  (z8  z5 )  (z6  z5 )
2 2

## Slide 26: Gradient Operators
DIP, Spring 2012 GS & AS, Bahria University, Islambad
Prewitt Operator
f  (z7  z8
 z9 )  (z1  z2  z3 )
 (z3  z6  z9 )  (z1  z4  z7 )
-1 | -1 | -1
0 | 0 | 0
1 | 1 | 1
f
x 
-1 | 0 | 1
-1 | 0 | 1
-1 | 0 | 1
f
y 
Extract horizontal edges
Extract vertical edges
is used for detecting edges horizontally and vertically.
Pixel Arrangement

## Slide 27: Gradient Operators
DIP, Spring 2012 GS & AS, Bahria University, Islambad
-1
 |  | -2 | -1 | f  x | -1 | 0 |  | 1 |  | 
0 |  | 0 | 0 |  | -2 | 0 |  | 2 |  | 
1 |  | 2 | 1 |  | -1 | 0 |  | 1 |  | 
f
y 
Extract horizontal edges
f  (z7  2z8  z9 )  (z1  2z2
 (z3  2z6  z9 )  (z1  2z4
 z3 )
 z7 )
Emphasize more the current point (x direction)
Emphasize more the current point (y
direction)
Pixel Arrangement
Extract vertical edges
Sobel Operator
Same as Prewitt Operator

## Slide 28: Sobel Operator: Example
DIP, Spring 2012 GS & AS, Bahria University, Islambad
Sobel filters are typically used for edge
detection
An image of a contact lens which is enhanced in order to make defects more obvious

## Slide 29: Sharpening
30

## Slide 30: Other filters
1 | 0 | -1
2 | 0 | -2
1 | 0 | -1
Vertical Edge
(absolute value) 31
Sobel
2016/1/27

## Slide 31: Other filters
1 | 2 | 1
0 | 0 | 0
-1 | -2 | -1
Horizontal Edge
(absolute value) 32
Sobel
2016/1/27

## Slide 32: Basic gradient filters
0 | 0 | 0
-1 | 0 | 1
0 | 0 | 0
0 | 1 | 0
0 | 0 | 0
0 | -1 | 0
-1 | 0 | 1
or
Horizontal Gradient
Vertical Gradient
-1
0
1
or
33
2016/1/27

## Slide 33: Difference Filter
DIP, Spring 2012 GS & AS, Bahria University, Islambad 34
Diagonal 2
Horizontal
Diagonal 1
Vertical
Also called as emboss filters
Enhances the details in the direction specific to the mask selected
Four primary difference filter convolution masks, corresponding to the edges in the vertical, horizontal, and two diagonal directions are:

## Slide 34: Difference Filter
DIP, Spring 2012 GS & AS, Bahria University, Islambad 35
Original image
Difference filtered image
Difference filtered image added to the original image, with contrast enhanced

## Slide 35: Next slides are extra material for study!!!
DIP, Spring 2012 GS & AS, Bahria University, Islambad

## Slide 36: Combining Spatial Enhancement Methods
DIP, Spring 2012 GS & AS, Bahria University, Islambad
Successful image enhancement is
typically not achieved using a single
operation
Rather we combine a range of
techniques in order to achieve a final
result
This example will focus on enhancing
the bone scan

## Slide 37: Combining Spatial Enhancement Methods
(a)
Laplacian filter of
bone scan (a)
(b)
Sharpened version of bone scan achieved by subtracting (a) and (b)
(c)
Sobel filter of bone scan (a)
(d)

## Slide 38: Combining Spatial Enhancement Methods
Sharpened
Result of applying a
power-law trans. to image (g)
The product of (c) and (e) which will be used as a mask
(e)
which is sum of (a)
and (f)
(f)
(g)
(h)
Image (d) smoothed with a 5*5 averaging filter

## Slide 39: Combining Spatial Enhancement Methods
Compare the original and final images